## Slide 1: Something IS better than Zero: Integrating Continual Improvement and Zero Energy Goals Presented At ACEEE Industrial Energy Efficiency Summer Study 13 August 2019
David B. Goldstein, Ph.D.
Natural Resources Defense Council
dgoldstein@nrdc.org

## Slide 2: Climate Change: Melting Glaciers

## Slide 3: Climate Change: Forest Fires
Notes: Reddest sunrise in decades—produced by smoke particulates from forest fires 50 miles away. The fires are a likely result of climate change. We have also seen such fires in the Northwest, and hurricanes in Puerto Rico, the Caribbean, Florida, and Texas.

## Slide 4: Introduction to Zero Net Energy (ZNE)
Zero net energy goals are an important tool for meeting globally accepted climate goals (see next slide)
This paper describes 4 levels of “zero” with increasing levels of ambition
These levels can be integrated with the continual improvement goals in ISO 50001 and “Strategic Energy Management”
Notes: These four levels are seen in a number of program plans and ideas but are not usually presented as a consistent package.

## Slide 5: U.S. Pathways to Paris’ Long-term Goals
Chart: Total Greenhouse Gases (MMT CO2eq) with LUCF
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Historical (w/ LUCF) | 5543.4636 | 5479.4234 | 5608.7403 | 5738.6671 | 5801.6068 | 5923.2759 | 6103.1861 | 6178.3746 | 6249.5752 | 6296.3017 | 6461.5035 | 6373.5481 | 6425.6033 | 6458.0414 | 6605.9648 | 6582.3181 | 6505.2343 | 6650.5665 | 6460.3624 | 6008.6128 | 6208.2684 | 6027.5746 | 5784.5161 | 5917.072 | 5978.3264 | 5827.7249
BAU (w/ LUCF) | 5827.7249 | 5687.3514 | 5721.6012 | 5775.0208 | 5852.883 | 5937.1248 | 5915.3255 | 5860.2173 | 5838.9861 | 5825.0369 | 5832.7111 | 5796.3759 | 5742.935 | 5705.1691 | 5677.2081 | 5669.0279 | 5657.2407 | 5643.9953 | 5640.75 | 5645.709 | 5654.0639 | 5663.9678 | 5673.0566 | 5683.9977 | 5699.0532 | 5709.2919 | 5723.4687 | 5741.2793 | 5763.2609 | 5786.2338 | 5809.9418 | 5838.6205 | 5866.4363 | 5898.0197 | 5944.4707 | 6043.1816
2 Degree Trajectory (w/ LUCF) | 5827.7249 | 5599.8326 | 5530.3851 | 5458.2241 | 5385.3302 | 5287.4543 | 5143.6036 | 4998.0276 | 4831.9469 | 4644.6244 | 4359.1942 | 4180.9293 | 4016.1788 | 3792.872 | 3622.6514 | 3430.0566 | 3279.9042 | 2860.4175 | 2749.9131 | 2596.9438 | 2495.7046 | 2357.113 | 2247.6256 | 2143.902 | 2040.0829 | 1934.7194 | 1820.6878 | 1709.7107 | 1610.1755 | 1519.7945 | 1435.8142 | 1358.3289 | 1283.1775 | 1207.5107 | 1124.7093 | 988.0748
1.5 Degree Trajectory (Higher Contribution from Developed) | 5827.7249 | 5519.4164 | 5437.9565 | 5144.5717 | 4928.598 | 4727.6335 | 4493.6246 | 4265.1648 | 4027.6949 | 3767.2071 | 3418.1583 | 3183.5428 | 2968.1938 | 2715.0122 | 2503.4028 | 2276.4007 | 2110.6184 | 1796.843 | 1678.3324 | 1536.4411 | 1423.678 | 1293.6945 | 1183.6108 | 1079.602 | 978.4736 | 880.7479 | 787.0607 | 697.6056 | 616.1812 | 541.33 | 454.2577 | 371.4699 | 290.2889 | 202.0782 | 105.8716 | 0
2025 NDC Target | 4397
2050 MCS Target (2005) | 1572
2050 NRDC Target (1990) | 1023

## Slide 6: “Nothing is better than zero”
Zero Net Energy has attracted rapidly growing interest around the world
Growth rates of projected and verified Zero Energy buildings are continuing to be high
  Some industrial facilities claim Zero Energy performance
Zero Energy is an easily understood concept that helps make efficiency visible
Zero Energy buildings may not cost more to build than conventional practice, but they provide non-energy benefits such as comfort, health, etc.
  Zero Energy industrial plants may also provide improved profitability and quality

## Slide 7: But…
What do we mean by zero?
  Zero Net Energy does not mean zero energy bills
  After Zero Net Energy facilities--or even stand-alone solar and wind energy--become common, Zero Net Energy does not mean zero emissions from the grid
Key questions this talk will address:
  What is the scope of a Zero Energy facility: how do you count energy?
  How can you zero out emissions?
    What if you count supply chain energy of construction of the facility?
    What if you count transportation energy to service it?
  How does a Zero Energy goal fit into an Energy Management System that is built around continual improvement?

## Slide 8: How do we net out production and consumption?
Current definitions globally look at accumulated annual energy consumption and accumulated on-site renewable energy production
When production equals consumption this is called Zero Net Energy
But this metric has complexities that will be discussed next

## Slide 9: Zero Net Energy is the same thing as 100% renewable energy, right?
Not exactly:
  100% renewables can be achieved by just spending money, while ZNE requires thought and action within the facility
  100% renewables might include renewable energy far removed from the plant site (such as solar in Sri Lanka for a plant in Alabama)
    Are the offsite renewables additional? How do we know?
ZNE buildings almost always are extremely efficient: efficiency comes first and renewables second
Notes: Remember that the motivation is climate, which is global. Individual accomplishment means nothing unless it is a building block to global accomplishment.

## Slide 10: Renewable Energy Production: where do we draw the boundaries?
Geographically:
  At the unit?
  At the property?
  At the subdivision?
  At some specified distance?
  What about RECs?
Temporally:
By the year for the first year?
Continually by the year for N years into the future?
Measured by annual average or on an hourly or 15-minute basis?

## Slide 11: How do existing ZNE Standards draw these geographic boundaries?
Offsite renewables are generally discouraged if not outright disallowed
  The use of Renewable Energy Credits (RECs) is usually prohibited or deeply discounted; and
  RECs from onsite renewables must be retired, not sold
The issue is complex: questions include ownership of the renewables, treatment of RECs, connection of the renewables to the facility, control over the renewables, distance from the site…
Consistent standards would be helpful

## Slide 12: How do existing ZNE Standards draw these temporal boundaries?
Current standards look at annual averages and consider only one year, or look at achievement of ZNE one year at a time
This paper looks at long-term plans over ten years or longer
It also recommends consideration of short-term (hourly or shorter) energy balance

## Slide 13: The Electric Grid

## Slide 14: Diurnal Variation: the “Duck Curve”
Notes: (Animated) In CA, this phenomenon is called the ‘Duck Curve’

## Slide 15: This is the duck: (net electricity loads in California vs. time of day)

## Slide 16: California GHG Emissions Factors 2018
* CPUC Avoided Cost Model 2018: http://www.cpuc.ca.gov/General.aspx?id=5267
Chart: Hourly Emissions Factor (2030)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Total | 0.42666 | 0.42666 | 0.42666 | 0.42666 | 0.42666 | 0.42666 | 0.42666 | 0.013763 | 0.013763 | 0.041492 | 0.083187 | 0.18362 | 0.28466 | 0.3706 | 0.3706 | 0.38436 | 0.40107 | 0.59109 | 0.69176 | 0.55669 | 0.44336 | 0.42666 | 0.42666 | 0.42666
Notes: GHGs merit their own slide because they are more complicated
GHG benefits significant, but smaller than you would intuitively expect based on duck curve.
This slide different from paper, updated from 2017 to 2018 ACM => Better GHG benefits than 2017, but still not very high
To assess GHG benefits, need hourly emissions factor
Currently available hourly emissions factors (CPUC, CEC) use average, or short-run/dispatch marginal accounting methodologies
Average isn’t right way to account for policy impacts (avoided GHGs)
Short-run marginal doesn’t account for impacts of large-scale electrification policies, require building new generation
New generation will be mostly carbon free (RPS, SB 100), entirely carbon-free in solar hours. Not reflected in CPUC emissions factors
Takeaway: GHG benefits of large scale managed HPWH adoption

## Slide 17: Energy efficiency remains essential to address annual variation
Potential Shift to Winter Peak Under High Electrification Scenario
NEEP: Northeastern Regional Assessment of Strategic Electrification, July 2017
https://neep.org/strategic-electrification-regional-assessment
Notes: Northeast, not CA: explain chart: summer to winter peak, increase system peak, new power plants and poles and wires => system costs:
  Direct customer costs (higher use)
  Grid costs => impacts all customers through higher rates
Instead, want to fill valleys: no incremental fixed costs, higher sales, downward pressure on rates.

## Slide 18: Opportunities for Consumer Integration with Grid
Permanent Efficiency
  Reduce energy loads…
Peak Shifting
  Design to modify time of peak energy use to adapt to grid…
Dynamic Response
  Actively reduce energy use in response to short-term grid constraints…
Dispatchable Energy Storage
  Actively manage energy use patterns based on grid signals…
Notes: By deploying building/grid integration strategies, utilities can hedge against some price volatility while reducing private incentive to hedge independently of utility interests.

## Slide 19: Facility Load Curve
Base Load
Storage
ADR
Load Factor
Energy Efficiency
Peak Shift
Notes: (Animated): Building load shape can be manipultated to improve grid-interaction. This is a conceptual description of how GO will impact building load shape.

## Slide 20: Teaching the Duck to Fly”
Notes: Based on Jim Lazar’s analysis of how deploying demand response technologies can impact the load curve.

## Slide 21: Seasonal variation

## Slide 22: Process design evaluation should include load shape predictions so that fixed and adjustable building features can be incorporated to manage load shape.
3D Electric Profile, Full Year
Energy Modeling

## Slide 23: Integrating ZNE and SEM
This paper defines four levels of ZNE and suggests continual improvement from the lowest level to higher levels:
ZNE as annual average
ZNE considering the energy inputs to the grid and a time of use basis
ZNE considering in addition the energy required to construct the facility
ZNE considering in addition transportation energy of supplies and people to the site

## Slide 24: Zero Energy and Continual Improvement
Definitions of zero energy often focus on metered energy use
If energy performance (which doesn’t count renewables) is continually improving, net zero in year N means net consumption in years N-1, N-2…etc.
  And it also implies net positive contribution to the grid in years N+1, N+2…
Designers can specify an energy policy for continual improvement that brings the facility to Zero Net in a planned year
Outcomes are projected using a very simplified model (see Annex 1)

## Slide 25: Carbon Emissions over Time
Chart: Gross and Net carbon emissions with Continual Improvement in Energy Performance (3%/year)
net carbon emissions | 40 | 37 | 34.09 | 31.2673 | 28.5293 | 25.8734 | 23.2972 | 20.7983 | 18.3743 | 16.0231 | 13.7424 | 11.5301 | 9.3842 | 7.3027 | 5.2836 | 3.3251 | 1.4254 | -0.4174 | -2.2049 | -3.9387 | -5.6206 | -7.2519 | -8.8344 | -10.3694 | -11.8583 | -13.3025 | -14.7035 | -16.0623 | -17.3805 | -18.6591 | -19.8993 | -21.1023 | -22.2692 | -23.4012 | -24.4991 | -25.5642 | -26.5972 | -27.5993 | -28.5713 | -29.5142 | -30.4288 | -31.3159 | -32.1764 | -33.0111 | -33.8208 | -34.6062 | -35.368 | -36.107 | -36.8237 | -37.519 | -38.1935 | -38.8477 | -39.4822 | -40.0978 | -40.6948 | -41.274 | -41.8358 | -42.3807
net carbon before solar | 100 | 97 | 94.09 | 91.2673 | 88.5293 | 85.8734 | 83.2972 | 80.7983 | 78.3743 | 76.0231 | 73.7424 | 71.5301 | 69.3842 | 67.3027 | 65.2836 | 63.3251 | 61.4254 | 59.5826 | 57.7951 | 56.0613 | 54.3794 | 52.7481 | 51.1656 | 49.6306 | 48.1417 | 46.6975 | 45.2965 | 43.9377 | 42.6195 | 41.3409 | 40.1007 | 38.8977 | 37.7308 | 36.5988 | 35.5009 | 34.4358 | 33.4028 | 32.4007 | 31.4287 | 30.4858 | 29.5712 | 28.6841 | 27.8236 | 26.9889 | 26.1792 | 25.3938 | 24.632 | 23.893 | 23.1763 | 22.481 | 21.8065 | 21.1523 | 20.5178 | 19.9022 | 19.3052 | 18.726 | 18.1642 | 17.6193

## Slide 26: Carbon Emissions over Time
Chart: Gross and Net carbon emissions with Continual Improvement in Energy Performance (5%/year)
net carbon before solar | 100 | 95 | 90.25 | 85.7375 | 81.4506 | 77.3781 | 73.5092 | 69.8337 | 66.342 | 63.0249 | 59.8737 | 56.88 | 54.036 | 51.3342 | 48.7675 | 46.3291 | 44.0127 | 41.812 | 39.7214 | 37.7354 | 35.8486 | 34.0562 | 32.3534 | 30.7357 | 29.1989 | 27.739 | 26.352 | 25.0344 | 23.7827 | 22.5936 | 21.4639 | 20.3907 | 19.3711 | 18.4026 | 17.4825 | 16.6083 | 15.7779 | 14.989 | 14.2396 | 13.5276 | 12.8512 | 12.2087 | 11.5982 | 11.0183 | 10.4674 | 9.944 | 9.4468 | 8.9745 | 8.5258 | 8.0995 | 7.6945 | 7.3098 | 6.9443 | 6.5971 | 6.2672 | 5.9539 | 5.6562 | 5.3734 | 5.1047
net carbon emissions | 40 | 35 | 30.25 | 25.7375 | 21.4506 | 17.3781 | 13.5092 | 9.8337 | 6.342 | 3.0249 | -0.12631 | -3.12 | -5.964 | -8.6658 | -11.2325 | -13.6709 | -15.9873 | -18.188 | -20.2786 | -22.2646 | -24.1514 | -25.9438 | -27.6466 | -29.2643 | -30.8011 | -32.261 | -33.648 | -34.9656 | -36.2173 | -37.4064 | -38.5361 | -39.6093 | -40.6289 | -41.5974 | -42.5175 | -43.3917 | -44.2221 | -45.011 | -45.7604 | -46.4724 | -47.1488 | -47.7913 | -48.4018 | -48.9817 | -49.5326 | -50.056 | -50.5532 | -51.0255 | -51.4742 | -51.9005 | -52.3055 | -52.6902 | -53.0557 | -53.4029 | -53.7328 | -54.0461 | -54.3438 | -54.6266 | -54.8953

## Slide 27: Cumulative Carbon Emissions
Chart: Cumulative Emission including embodied emissions from construction and remodeling

## Slide 28: It takes a lot more solar…
Chart: Cumulative Carbon Emissions
cum carbon with doubled solar | 9980 | 9957 | 9931.09 | 9902.3573 | 9870.8866 | 9836.76 | 9800.0572 | 9760.8555 | 9719.2298 | 9675.2529 | 9628.9953 | 9580.5255 | 9529.9097 | 9477.2124 | 9422.496 | 9365.8212 | 9307.2465 | 9246.8291 | 9184.6243 | 9120.6855 | 9055.065 | 8987.813 | 8918.9786 | 8848.6093 | 8776.751 | 9703.4485 | 9628.745 | 9552.6826 | 9475.3022 | 9396.6431 | 9316.7438 | 9235.6415 | 9153.3723 | 9069.9711 | 8985.472 | 8899.9078 | 8813.3106 | 8725.7112 | 8637.1399 | 8547.6257 | 8457.1969 | 8365.881 | 8273.7046 | 8180.6935 | 8086.8727 | 7992.2665 | 7896.8985 | 7800.7915 | 7703.9678 | 7606.4487 | 7508.2553 | 7409.4076 | 7309.9254 | 7209.8276 | 7109.1328 | 8007.8588 | 7906.0231 | 7803.6424
cum carbon with 10x solar | 9440 | 8877 | 8311.09 | 7742.3573 | 7170.8866 | 6596.76 | 6020.0572 | 5440.8555 | 4859.2298 | 4275.2529 | 3688.9953 | 3100.5255 | 2509.9097 | 1917.2124 | 1322.496 | 725.8212 | 127.2465 | -473.1709 | -1075.3757 | -1679.3145 | -2284.935 | -2892.187 | -3501.0214 | -4111.3907 | -4723.249 | -4336.5515 | -4951.255 | -5567.3174 | -6184.6978 | -6803.3569 | -7423.2562 | -8044.3585 | -8666.6277 | -9290.0289 | -9914.528 | -10540.0922 | -11166.6894 | -11794.2888 | -12422.8601 | -13052.3743 | -13682.8031 | -14314.119 | -14946.2954 | -15579.3065 | -16213.1273 | -16847.7335 | -17483.1015 | -18119.2085 | -18756.0322 | -19393.5513 | -20031.7447 | -20670.5924 | -21310.0746 | -21950.1724 | -22590.8672 | -22232.1412 | -22873.9769 | -23516.3576

## Slide 29: Transportation may not change crossover much (with lots of solar generation)
Chart: 
cum carbon with 10x solar | 9500 | 8995 | 8485.25 | 7970.9875 | 7452.4381 | 6929.8162 | 6403.3254 | 5873.1591 | 5339.5012 | 4802.5261 | 4262.3998 | 3719.2798 | 3173.3158 | 2624.65 | 2073.4175 | 1519.7467 | 963.7593 | 405.5714 | -154.7072 | -716.9718 | -1281.1233 | -847.0671 | -1414.7137 | -1983.978 | -2554.7791 | -3127.0402 | -3700.6882 | -4275.6538 | -4851.8711 | -5429.2775 | -6007.8137 | -6587.423 | -7168.0518 | -7749.6492 | -8332.1668 | -8915.5584 | -9499.7805 | -10084.7915 | -10670.5519 | -11257.0243 | -11844.1731 | -12431.9644 | -13020.3662 | -13609.3479 | -14198.8805 | -14788.9365 | -15379.4897 | -15970.5152 | -16561.9894 | -17153.89 | -17746.1955 | -17338.8857 | -17931.9414 | -18525.3443 | -19119.0771 | -19713.1233 | -20307.4671 | -20902.0937


cum with solar and also transportation | 9115 | 8725.25 | 8330.9875 | 7932.4381 | 7529.8162 | 7123.3254 | 6713.1591 | 6299.5012 | 5882.5261 | 5462.3998 | 5039.2798 | 4613.3158 | 4184.65 | 3753.4175 | 3319.7467 | 2883.7593 | 2445.5714 | 2005.2928 | 1563.0282 | 1118.8767 | 1672.9329 | 1225.2863 | 776.022 | 325.2209 | -127.0402 | -580.6882 | -1035.6538 | -1491.8711 | -1949.2775 | -2407.8137 | -2867.423 | -3328.0518 | -3789.6492 | -4252.1668 | -4715.5584 | -5179.7805 | -5644.7915 | -6110.5519 | -6577.0243 | -7044.1731 | -7511.9644 | -7980.3662 | -8449.3479 | -8918.8805 | -9388.9365 | -9859.4897 | -10330.5152 | -10801.9894 | -11273.89 | -11746.1955 | -11218.8857 | -11691.9414 | -12165.3443 | -12639.0771 | -13113.1233 | -13587.4671 | -14062.0937 | -14536.9891

## Slide 30: Conclusions
The Zero Net Energy concept is proving an attractive way of making efficiency visible and encouraging renewable energy use
Zero Net Energy will not result in zero utility bills nor in zero carbon emissions, but
Continual improvement can allow zero emissions at a projected year in the foreseeable future
Zeroing out construction energy and transportation makes the goal much more difficult and requires much greater use of renewables

## Slide 31: Thank you
Please contact me at
DGoldstein@NRDC.org
for questions or comments

## Slide 32: Annex 1

## Slide 33: [Assumptions for model]
Zero energy building uses 40% of the energy of a conventional building
The conventional building creates about as much emissions to construct as it does to operate over 50 years
The carbon intensity of emissions avoided by solar on-site is 60% of the grid average
Energy consumption before counting solar declines at 3% (alternately 5%) annually
Transportation emissions are about half the operational emissions of the conventional building
Grid emissions intensity stays constant in the model, but energy performance improvements may include Demand Response

## Slide 34: Annex 2

## Slide 35: Meeting Long Term Climate Goals –California’s Experience
Chart: Electricity Consumption Per Capita (kWh/person)
| 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Other 49 States | 3827.6754 | 3944.9039 | 4205.5017 | 4447.5459 | 4714.4009 | 4957.3893 | 5313.5663 | 5582.3555 | 6057.269 | 6571.5241 | 6882.9445 | 7173.505 | 7711.4344 | 8233.1603 | 8171.4796 | 8222.1279 | 8665.1566 | 9043.3474 | 9288.0299 | 9422.8337 | 9472.2353 | 9633.9189 | 9285.2445 | 9527.1158 | 10031.1158 | 10117.3267 | 10248.9024 | 10556.3898 | 11004.8157 | 11225.4565 | 11387.7246 | 11475.2261 | 11305.886 | 11594.2794 | 11746.0502 | 11939.0823 | 12145.4009 | 12149.0596 | 12466.9438 | 12532.5555 | 12802.9409 | 12562.1754 | 12780.2743 | 12754.6472 | 12811.3109 | 13118.4571 | 12985.8717 | 13209.7237 | 12953.0336 | 12368.9592 | 12853.1795 | 12734.0382 | 12451.7415 | 12364.5193 | 11817.2893
California | 3608.697 | 3781.6525 | 3802.1421 | 3935.3557 | 4241.553 | 4449.1141 | 4820.9374 | 5057.5451 | 5394.2177 | 5655.1044 | 5930.1965 | 6184.7629 | 6572.8118 | 6710.7115 | 6207.7564 | 6891.131 | 7112.3976 | 7104.5239 | 7122.3945 | 7291.9981 | 7040.3344 | 7016.9691 | 6681.8301 | 6514.1474 | 6943.6879 | 6971.4177 | 6841.5295 | 6940.9929 | 7048.8046 | 6986.7469 | 7045.8252 | 6847.5104 | 6890.9521 | 6730.6131 | 6787.076 | 6707.4084 | 6811.9705 | 7014.7179 | 7167.272 | 7010.0862 | 7180.6874 | 7185.7878 | 6745.0485 | 6899.3083 | 7084.3562 | 7096.3913 | 7300.1451 | 7289.2389 | 7325.8447 | 7023.1764 | 6924.072 | 6951.0137 | 6831.5789 | 6703.7266 | 6788.5083