## Slide 1: Approaches to Scenario Development
Simply adjust outflow/inflow by a specific quantity of water
  too difficult w/CalSIM
Applying a straight % reduction in diversion
  reduction needs were too small for CalSIM to respond (i.e., within CalSIM error bars)
Reduce outflow targets to identify associated water costs
  preferred approach

## Slide 2: Scenarios
Schedule A – Year-round Increases Delta Outflows
Schedule B – Reduced Winter (Jan/Feb) Flows
Schedule C – Spring Outflow Enhancement + Summer Delta Smelt Flows
Schedule D – Spring Outflow Enhancement
Schedules E-G – Reduced Spring Outflow

## Slide 3: Model Assumptions
Outflow targets adjusted (Schedules B-G)
No pre-assigned reduction in diversions
Reservoir storage adjusted to maintain cold water pool
  Folsom 400 TAF
  Oroville 1.0 MAF
  Shasta 2.2 MAF
CalSIM weighting adjusted to prioritize reservoir storage levels over outflow and diversions

## Slide 4
Month | W | AN | BN | D | C
Oct | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | 5,000 (84km) | D-1641 | D-1641
Nov | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | 5,000 (84km) | D-1641 | D-1641
Dec | 11,400 (75Km) | 5,000 (84km) | 5,000 (84km) | D-1641 | D-1641
Jan | 35,000 |  |  |  | 
Feb |  |  |  |  | 
Mar | 44,500 |  | 25,000 | 11,400 (74km) | 11,400 (74km)
Apr |  |  |  |  | 
May |  |  |  |  | 
Jun | D-1641 or 12,400 (74km)1 | D-1641 or 11,400 (75km)1 | D-1641 or 11,400 (75km)1 | D-1641 | D-1641
Jul | 12,400 (74km) | D-1641 | 7,500 80km) | D-1641 | D-1641
Aug | 12,400 (74km) | 7,500 (80km) | 5,000 (84km) | D-1641 | D-1641
Sep | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | 5,000 (84km) | D-1641 | D-1641
Improved Flow Values [bold] and Associated Targeted Species Objectives (below) |  |  |  |  | 
D-1641 |  | Existing SWRCB D1641 requirements |  |  | 
BiOp RPA |  | Fall X2 requirements (Delta Smelt) |  |  | 
Delta Smelt |  | Improve spawning and rearing habitat conditions by placing the LSZ around suitable abiotic habitat |  |  | 
Longfin Smelt |  | Increase LFS abundance |  |  | 
Fall/Late Fall-run Chinook |  | Increased fry survival |  |  | 
Sturgeon |  | Attraction flows |  |  | 
1 Whichever flow value is higher |  |  |  |  | 
Schedule A – Year-round Increases Delta Outflows
Improved survival and potential for year after year population growth (LFS/CHNK/STLHD)
Benefits sturgeon by providing better environmental conditions to increase the likelihood of successful sturgeon year classes (attraction flows)
Benefits Delta smelt through improved survival and potential for year after year population growth
~1.98 MAF

## Slide 5
Month | W | AN | BN | D | C
Oct | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | 5,000 (84km) | D-1641 | D-1641
Nov | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | 5,000 (84km) | D-1641 | D-1641
Dec | 11,400 (75Km) | 5,000 (84km) | 5,000 (84km) | D-1641 | D-1641
Jan | 25,000 | 25,000 | 20,000 | 15,000 | 15,000
Feb | 25,000 | 25,000 | 20,000 | 15,000 | 15,000
Mar | 44,500 |  | 25,000 | 11,400 (74km) | 11,400 (74km)
Apr |  |  |  |  | 
May |  |  |  |  | 
Jun | D-1641 or 12,400 (74km)1 | D-1641 or 11,400 (75km)1 | D-1641 or 11,400 (75km)1 | D-1641 | D-1641
Jul | 12,400 (74km) | D-1641 | 7,500 80km) | D-1641 | D-1641
Aug | 12,400 (74km) | 7,500 (80km) | 5,000 (84km) | D-1641 | D-1641
Sep | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | 5,000 (84km) | D-1641 | D-1641
Improved Flow Values [bold] and Associated Targeted Species Objectives (below) |  |  |  |  | 
D-1641 |  | Existing SWRCB D1641 requirements |  |  | 
BiOp RPA |  | Fall X2 requirements (Delta Smelt) |  |  | 
Delta Smelt |  | Improve spawning and rearing habitat conditions by placing the LSZ around suitable abiotic habitat |  |  | 
Longfin Smelt |  | Increase LFS abundance |  |  | 
Fall/Late Fall-run Chinook |  | Increased fry survival |  |  | 
Sturgeon |  | Attraction flows |  |  | 
1 Whichever flow value is higher |  |  |  |  | 
Schedule B– Reduced Winter (Jan/Feb) Flows
Improved survival and potential for year after year population growth (LFS/CHNK/STLHD)
Benefits sturgeon by providing better environmental conditions to increase the likelihood of successful sturgeon year classes (attraction flows)
Benefits Delta smelt through improved survival and potential for year after year population growth
~1.35 MAF

## Slide 6
Month | W | AN | BN | D | C
Oct | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | 5,000 (84km) | D-1641 | D-1641
Nov | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | 5,000 (84km) | D-1641 | D-1641
Dec | 11,400 (75Km) | 5,000 (84km) | 5,000 (84km) | D-1641 | D-1641
Jan | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Feb | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Mar | 44,500 |  | 25,000 | 11,400 (74km) | 11,400 (74km)
Apr |  |  |  |  | 
May |  |  |  |  | 
Jun | D-1641 or 12,400 (74km)1 | D-1641 or 11,400 (75km)1 | D-1641 or 11,400 (75km)1 | D-1641 | D-1641
Jul | 12,400 (74km) | D-1641 | 7,500 80km) | D-1641 | D-1641
Aug | 12,400 (74km) | 7,500 (80km) | 5,000 (84km) | D-1641 | D-1641
Sep | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | 5,000 (84km) | D-1641 | D-1641
Improved Flow Values [bold] and Associated Targeted Species Objectives (below) |  |  |  |  | 
D-1641 |  | Existing SWRCB D1641 requirements |  |  | 
BiOp RPA |  | Fall X2 requirements (Delta Smelt) |  |  | 
Delta Smelt |  | Improve spawning and rearing habitat conditions by placing the LSZ around suitable abiotic habitat |  |  | 
Longfin Smelt |  | Increase LFS abundance |  |  | 
Fall/Late Fall-run Chinook |  | Increased fry survival |  |  | 
Sturgeon |  | Attraction flows |  |  | 
1 Whichever flow value is higher |  |  |  |  | 
Schedule C – Spring Outflow Enhancement + Summer Delta Smelt Flows
Improved survival and potential for year after year population growth (LFS/CHNK/STLHD)
Benefits Delta smelt through improved survival and potential for year after year population growth
~1.3 MAF

## Slide 7
Month | W | AN | BN | D | C
Oct | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Nov | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Dec | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Jan | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Feb | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Mar | 44,500 |  | 25,000 | 11,400 (74km) | 11,400 (74km)
Apr |  |  |  |  | 
May |  |  |  |  | 
Jun | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Jul | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Aug | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Sep | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Improved Flow Values [bold] and Associated Targeted Species Objectives (below) |  |  |  |  | 
D-1641 |  | Existing SWRCB D1641 requirements |  |  | 
BiOp RPA |  | Fall X2 requirements (Delta Smelt) |  |  | 
Delta Smelt |  | Improve spawning and rearing habitat conditions by placing the LSZ around suitable abiotic habitat |  |  | 
Longfin Smelt |  | Increase LFS abundance |  |  | 
Sturgeon |  | Attraction flows |  |  | 
1 Whichever flow value is higher |  |  |  |  | 
Schedule D – Spring Outflow Enhancement
Improved survival and potential for year after year population growth (LFS/CHNK/STLHD)
~1.0 MAF

## Slide 8
Month | W | AN | BN | D | C
Oct | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Nov | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Dec | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Jan | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Feb | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Mar | 44,500 |  | D-1641 | D-1641 | D-1641
Apr |  |  |  |  | 
May |  |  |  |  | 
Jun | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Jul | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Aug | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Sep | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Improved Flow Values [bold] and Associated Targeted Species Objectives (below) |  |  |  |  | 
D-1641 |  | Existing SWRCB D1641 requirements |  |  | 
BiOp RPA |  | Fall X2 requirements (Delta Smelt) |  |  | 
Longfin Smelt |  | Increase LFS abundance |  |  | 
1 Whichever flow value is higher |  |  |  |  | 
Schedule E - Reduced Spring Outflow
Improved survival and potential for year after year population growth of Longfin Smelt
~0.91 MAF

## Slide 9
Month | W | AN | BN | D | C
Oct | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Nov | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Dec | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Jan | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Feb | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Mar | 31,000 |  | D-1641 | D-1641 | D-1641
Apr |  |  |  |  | 
May |  |  |  |  | 
Jun | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Jul | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Aug | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Sep | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Improved Flow Values [bold] and Associated Targeted Species Objectives (below) |  |  |  |  | 
D-1641 |  | Existing SWRCB D1641 requirements |  |  | 
BiOp RPA |  | Fall X2 requirements (Delta Smelt) |  |  | 
Longfin Smelt |  |  |  |  | 
1 Whichever flow value is higher |  |  |  |  | 
Schedule F - Reduced Spring Outflow
~0.45 MAF

## Slide 10
Month | W | AN | BN | D | C
Oct | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Nov | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Dec | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Jan | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Feb | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Mar | 38,300 |  | D-1641 | D-1641 | D-1641
Apr |  |  |  |  | 
May |  |  |  |  | 
Jun | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Jul | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Aug | D-1641 | D-1641 | D-1641 | D-1641 | D-1641
Sep | D1641+BiOp Fall X2 | D1641+BiOp Fall X2 | D-1641 | D-1641 | D-1641
Improved Flow Values [bold] and Associated Targeted Species Objectives (below) |  |  |  |  | 
D-1641 |  | Existing SWRCB D1641 requirements |  |  | 
BiOp RPA |  | Fall X2 requirements (Delta Smelt) |  |  | 
Longfin Smelt |  |  |  |  | 
1 Whichever flow value is higher |  |  |  |  | 
Schedule G - Reduced Spring Outflow
~0.7 MAF

## Slide 11
Flow Schedule | Increased Delta Outflow | Total CVP/SWP Diversion Reduction
A | 1.98 MAF | 1.25 MAF
B | 1.35 MAF | 0.91 MAF
C | 1.3 MAF | 0.86 MAF
D | 1.0 MAF | 0.62 MAF
E | 0.91 MAF | 0.50 MAF
G* | 0.7 MAF | 0.35 MAF
F | 0.45 MAF | 0.17 MAF
Estimated average annual increase in total volume of water (acre foot) needed to achieve associated SWRCB’s % of unimpaired Delta outflow.
Schedule G* was not modeled, Mar-May flow of W and AN water years estimated at 38,000 cfs.
35% | 45% | 55% | 65% | 75%
694 TAF | 1.3 MAF | 2 MAF | 3.1 MAF | 4.6 MAF